FINAL TAKEHOME EXAM

Geology 4068 fall 2005

Please return answers by Monday December 12, 4.30 p.m.  You may leave the answers in my mailbox in E235 Howe-Russell.

You may do your work freehand, but please make sure your writing is legible so that I can understand your answers to the following questions fully and you can receive full due points for your work.

Question 1 (20 points) :  For the following idealized geological scenario below,and assuming you are dealing with zero-offset (stacked) seismic data (1) draw for cases A,B,C,D,E the reflection seismogram you would expect to receive at geophones on the surface.  Assume a zero-phase wavelet as shown below.  (10 points) Assume that the interfaces are practically horizontal.

(2) Now draw the reflection seismogram were you to use a 90-degree phase-shifted version of the same wavelet (10 points)

# Question 2 (10 Points)

Calculate the maximum fold for the following cases:

| Geophone spacing (m) | Number of geophones | Shot spacing (m) | Number of shots |
| --- | --- | --- | --- |
| 3 | 6 | 3 | 12 |
| 6 | 6 | 3 | 12 |
| 3 | 6 | 6 | 12 |
| 3 | 6 | 9 | 12 |

Question 3 (20 points)

We have as an objective to image using reflection seismology, a lens-shaped, sandy aquifer embedded in shale, at a shallowest depth of 200 m

The setting has steep faults that cut the lens in two and displace its segments vertically with respect to each other.

The lens of sand is about 20 m thick at its thickest point and about 1000 m long. Your vertical resolution must be 10 m or better.

Design the experiment. Be sure to include the following

(1 point each for the following)

- geophone number and spacing,

- shot number and spacing.

- Explain what characteristics of the source signal must be in order to achieve good a vertical resolution of 10 m.

- What will the horizontal resolution be?

- How can you improve the horizontal resolution?

- What is the dominant frequency?

- What will your Nyquist frequency be?

- What should you make your sampling rate?

- What will your spatial aliasing be?

(11 points for the following)

In a quantitative fashion explain your error in the estimation of the size of the aquifer.

Question 4 (50 points)

If you had a fairly thick horizontal layer of basalt (approximately 200 m thick) whose top lies at 100 m depth embedded in sandstone (above and below)

(1) calculate the VRMS to the top and to the bottom of the layer. (5 points)

- Draw all the seismic events you would expect to see. (5 points)

- Draw the expected change in amplitude with offset you expect to see in a very long shotpoint gather ( say, maximum offset is 10 km, and geophone spacing is 25 m) (5 points)

- Calculate critical distance for the top interface. (5 points)

- Calculate the shape of each of your seismic events at no more than 3 points and enough to show the general shape of your events. (10 points)

- Calculate and draw how your seismic events would appear if you moved out your CMP data about 80% of total NMO velocity.  (10 points)

- Calculate at no more than 3 points and enough to show the general shape of your shallowest seismic reflection event in a SP gather if the layer were dipping 20 degrees to the right on the page. (10 points)

# Text boxes

Clay (low density, low velocity)

Well-cemented Sandstone (higher density, higher velocity)

Limestone (highest density, highest velocity)

Zero-phase ricker wavelet

A

B

C

D

E